VYUŽITIE PRÍSTROJA  NA  LOKALIZÁCIU GEOGRAFICKEJ POLOHY PRI SKÚMANÍ PRIESTOROVEJ PREMENLIVOSTI POĽNÝCH PODMIENOK

USING OF GPS RECEIVER IN INVESTIGATION OF FIELD CONDITIONS SPATIAL VARIABILITY

Vladimír RATAJ, Andrej URBANOVIČ

Department of Machinery and Production Systems,

University of Agriculture, Tr. A. Hlinku 2, 949 76 Nitra, Slovakia

## ABSTRACT

Preparation of basic materials for precision farming in stage of a plant production needs perfect survey of landscape terrain. Satellite system GPS with large number of receivers is actually used for this purpose. GPS signal receiver Topcon Turbo G1 is available for use in conditions of SPU in Nitra. Geographical position finding exactness testing results of listed device are considered. There are field experiments evaluation bases, as a part of research problem, prepared on Department of Machines and Production Systems of SPU in Nitra. They describe cropstands changes during vegetation and variability of soil conditions. Results, which are based on geographical position finding with device mentioned above, are processewd by ArcView software modules.

Key words

GPS,